## Slide 1
Instruction Format (Three address, Two Address, one address, zero
address)

## Slide 2: Instruction Formats
A computer will usually have a variety of instruction code formats. It is the function of the control unit within the CPU to interpret each instruction code and provide the necessary control functions needed to process the instruction. The format of an instruction is usually depicted in a rectangular box symbolizing the bits of the instruction as they appear in memory words or in a control register. The bits of the instruction are divided into groups called fields.
The most common fields found in instruction formats are:
1. An operation code field that specifies the operation to be performed.
2. An address field that designates a memory address or a processor register.
3. A mode field that specifies the way the operand or the effective address is determined.

## Slide 3: Register Address
Operations specified by computer instructions are executed on some data stored in memory or processor registers. Operands residing in memory are specified by their memory address. Operands residing in processor registers are specified with a register address. A register address is a binary number of k bits that defines one of 2^k registers in the CPU.
Thus a CPU with 16 processor registers RO through R15 will have a register address field of four bits.
The binary number 0101, for example, will designate register R5. Computers may have instructions of several different lengths containing varying number of addresses.
The number of address fields in the instruction format of a computer depends on the internal organization of its registers.
Most computers fall into one of three types of CPU organizations:
1. Single accumulator organization.
2. General register organization.
3. Stack organization.

## Slide 4: 1. Single accumulator organization.
All operations are performed with an implied accumulator register. The instruction format in this type of computer uses one address field.
For example, the instruction that specifies an arithmetic addition is defined by an assembly language instruction as ADD X where X is the address of the operand.
The ADD instruction in this case results in the operation
AC <--AC + M [X].
AC is the accumulator register and M [X] symbolizes the memory word located at address X.

## Slide 5: 2. General register organization.
The instruction format in this type of computer needs three register address fields. Thus the instruction for an arithmetic addition may be written in an assembly language as
ADD R 1 , R 2 , R3 to denote the operation
R 1 <---R2 + R3.
The number of address fields in the instruction can be reduced from three to two if the destination register is the same as one of the source registers. Thus the instruction ADD R 1 , R2 would denote the operation R 1 <---R 1 + R2.
Only register addresses for R 1 and R2 need be specified in this instruction.
Computers with multiple processor registers use the move instruction with a mnemonic MOV to symbolize a transfer instruction.
Thus the instruction MOV R 1 , R2 denotes the transfer R 1 <--R2 (or R2 <--R1, depending on the particular computer). Thus transfer-type instructions need two address fields to specify the source and the destination.
General register-type computers employ two or three address fields in their instruction format. Each address field may specify a processor register or a memory word. An instruction symbolized by ADD R 1 , X would specify the operation
Rl <--Rl + M[X]. It has two address fields, one for register R 1 and the other for the memory address X.

## Slide 6: 3. Stack organization.
Computers with stack organization would have PUSH and POP instructions which require an address field.
Thus the instruction PUSH X will push the word at address X to the top of the stack.
The stack pointer is updated automatically.
Operation-type instructions do not need an address field in stack-organized computers. This is because the operation is performed on the two items that are on top of the stack.
The instruction ADD in a stack computer consists of an operation code only with no address field.
This operation has the effect of popping the two top numbers from the stack, adding the numbers, and pushing the sum into the stack. There is no need to specify operands with an address field since all operands are implied to be in the stack.

## Slide 7
To illustrate the influence of the number of addresses on computer programs, we will evaluate the arithmetic statement X = (A + B) • (C + D) using zero, one, two, or three address instructions.
We will use the symbols ADD, SUB, MUL, and DIV for the four arithmetic operations;
MOV for the transfer-type operation;
LOAD and STORE for transfers to and from memory and AC register.
We will assume that the operands are in memory addresses A, B, C, and D, and the result must be stored in memory at address X.

## Slide 8: Three-Address Instructions
Computers with three-address instruction formats can use each address field to specify either a processor register or a memory operand. The program in assembly language that evaluates X = (A + B) • (C + D) is shown below, together with comments that explain the register transfer operation of each instruction.
It is assumed that the computer has two processor registers, R 1 and R2. The symbol M [A] denotes the operand at memory address symbolized by A. The advantage of the three-address format is that it results in short programs when evaluating arithmetic expressions. The disadvantage is that the binary-coded instructions require too many bits to specify three addresses. An example of a commercial computer that uses three-address instructions is the Cyber 170. The instruction formats in the Cyber computer are restricted to either three register address fields or two register address fields and one memory address field.

## Slide 9: Two-Address Instructions
Two-address instructions are the most common in commercial computers. Here again each address field can specify either a processor register or a memory word. The program to evaluate X = (A + B) • (C + D) is as follows:
The MOV instruction moves or transfers the operands to and from memory and processor registers. The first symbol listed in an instruction is assumed to be both a source and the destination where the result of the operation is transferred.

## Slide 10: One-Address Instructions
One-address instructions use an implied accumulator (AC) register for all data manipulation. For multiplication and division there is a need for a second register. However, here we will neglect the second register and assume that the AC contains the result of all operations. The program to evaluate X = (A + B) • (C + D) is
All operations are done between the AC register and a memory operand. T is the address of a temporary memory location required for storing the intermediate result.

## Slide 11: Zero-Address Instructions
A stack-organized computer does not use an address field for the instructions ADD and MUL. The PUSH and POP instructions, however, need an address field to specify the operand that communicates with the stack. The following program shows how X = (A + B) • (C + D) will be written for a stackorganized computer. (TOS stands for top of stack.)