## Slide 1: Writing into Cache
An important aspect of cache organization is concerned with memory write requests. When the CPU finds a word in cache during a read operation, the main memory is not involved in the transfer. There are two ways that the system can proceed.
write-through method : The simplest and most commonly used procedure is to update main memory with every memory write operation, with cache memory being up­dated in parallel if it contains the word at the specified address. This method has the advantage that main memory always contains the same data as the cache. This characteristic is important in systems with direct memory access transfers. It ensures that the data residing in main memory are valid at all times so that an 110 device communicating through DMA would receive the most recent updated data.
write-back method : In this method only the cache location is updated during a write operation. The location is then marked by a flag so that later when the word is removed from the cache it is copied into main memory. The reason for the write-back method is that during the time a word resides in the cache, it may be updated several times; however, as long as the word remains in the cache, it does not matter whether the copy in main memory is out of date, since requests from the word are filled from the cache. It is only when the word is displaced from the cache that an accurate copy need be rewritten into main memory. Analytical results indicate that the number of memory writes in a typical program ranges between 10 and 30 percent of the total references to memory.

## Slide 2: Cache Initialization
One more aspect of cache organization that must be taken into consideration is the problem of initialization.
The cache is initialized when power is applied to the computer or when the main memory is loaded with a complete set of programs from auxiliary memory.
After initialization the cache is considered to be empty, but in effect it contains some non valid data.
It is customary to include with each word in cache a valid bit to indicate whether or not the word contains valid data.
The cache is initialized by clearing all the valid bits to 0.
The valid bit of a particular cache word is set to 1 the first time this word is loaded from main memory and stays set unless the cache has to be initialized again.
The intro­duction of the valid bit means that a word in cache is not replaced by another word unless the valid bit is set to 1 and a mismatch of tags occurs.
If the valid bit happens to be 0, the new word automatically replaces the invalid data.
Thus the initialization condition has the effect of forcing misses from the cache until it fills with valid data.